## Slide 1: Bicycle Design Gudelines
Urban + Suburban Applications
October 11, 2019

## Slide 2
POLICY
Notes: Add logos to explain the cyclical relationship
FHWA Policy Memos
2010, encourage flexibility
2013, mentions ITE, AASHTO, and NACTO by name

## Slide 3: Policy
IDOT BDE, Chapter 17
  17-1.05 Maintenance and Jurisdiction
  17-1.07 Funding
IDOT BLRS, Chapter 42
  42-3.02(a) Bike Paths Versus Sidewalks
  42-4 Maintenance
POLICY
Notes: 17-1.05 Maintenance and Jurisdiction
Responsibility for ongoing maintenance of bikeway facilities within the roadway surface is assumed to be an integral part of roadway maintenance. Responsibility for maintenance of bikeway and pedestrian facilities separated from the roadway surface should be delegated by agreement with local/State jurisdictions or others early in the planning process; see Chapter 5.
17-1.07 Funding
Bicycle facilities for the safe travel of bicyclists within an improvement corridor, are considered an integral part of a highway project for funding purposes, and thus are eligible for cost participation as discussed in Chapter 5. If conditions within the roadway prohibit the inclusion of adequate bicycle accommodations, necessary off-roadway accommodations shall be included where they can be accommodated. Accommodations beyond those that are determined necessary from the Facility Selection Table in Figure 17-2.A may be desired or preferred by local officials, and the cost difference could be funded through several options as follows:
- initiated by others than IDOT and submitted as a candidate for the Transportation Enhancement Program funding (see Chapter 18);
- initiated by others than IDOT and submitted for consideration from other appropriate Federal funding categories (e.g., the Congestion Mitigation and Air Quality (CMAQ) or various Surface Transportation Program (STP) categories); or
- initiated by others than IDOT and funded entirely through outside governmental organizations.
42-4 MAINTENANCE
Responsibility for maintenance of bike lane facilities should be determined and agreed upon during the planning process and should be included in the local agency funding agreement, when applicable.

## Slide 4
POLICY
Notes: FHWA provides guidance on the status of approved traffic control devices per MUTCD
“As described in Paragraph 11 of Section 1A.10, all requests should include…”

## Slide 5: MUTCD 1A.10 Experimentations, Changes, and Interim Approvals
POLICY
Approved
  Acceptable for use as indicated
Interim Approval
  Notify FHWA to document your intent
  Item is likely to be included in next MUTCD, but rules may be revised
Request to Experiment
  MUTCDofficialrequest@dot.gov
  Statement of interpretation
  Description of condition that provokes need
  Illustrations and diagrams as needed
  Pertinent supporting research data
Notes: FHWA provides guidance on the status of approved traffic control devices per MUTCD
“As described in Paragraph 11 of Section 1A.10, all requests should include…”

## Slide 6: Principles
PRINCIPLES
Make it rideable
Make it inviting, comfortable
Make roadway users visible to each other
Design for all ages and abilities
Context matters
Notes: Rideable: smooth riding surface, no potholes, drainage grates should run perpendicular to the path of travel, don’t let manholes or vault covers protrude/recess
Inviting, comfortable: give adequate space and designate space exclusively for bicyclists, prevent speeding, reallocate roadway space, change land widths if needed
Aware/visible: make it easier for people driving to see people bicycling and vice versa – this is where geometry is key and pavement markings/signs can help
All ages and abilities: too stressful to take your child with you? Keep thinking about what would further reduce stress.

## Slide 7: Principles
PRINCIPLES
Metrics
  Level of Service (LOS/BLOS)
  Level of Traffic Stress (LTS/BLTS)
  Who is the Bicycling Population?
Image Source: Fehr & Peers, one.jack.design
Number of Lanes
Traffic Speed
Volume/Type
Exclusive Space
Facility Width
Buffers/Barriers
Notes: LTS is a qualitative measure that evaluates the level of stress a bicyclists feels when using a facility
- Inputs are quantifiable
- Stress tolerance tracks closely with confidence and experience level

## Slide 8: Principles
PRINCIPLES
Basics: Operating Width
  4’ minimum
  5’ preferred
  Additional separation needs will vary (buffers, curbs, bollards, flexposts/delineators, parked cars, medians)
Notes: Rideable: smooth riding surface, no potholes, drainage grates should run perpendicular to the path of travel, don’t let manholes or vault covers protrude/recess
Inviting, comfortable: give adequate space and designate space exclusively for bicyclists, prevent speeding, reallocate roadway space, change land widths if needed
Aware/visible: make it easier for people driving to see people bicycling and vice versa – this is where geometry is key and pavement markings/signs can help
All ages and abilities: too stressful to take your child with you? Keep thinking about what would further reduce stress.

## Slide 9
PRINCIPLES
Image Source: Kery Caffrey, Cycling Savvy
Notes: Rideable: smooth riding surface, no potholes, drainage grates should run perpendicular to the path of travel, don’t let manholes or vault covers protrude/recess
Inviting, comfortable: give adequate space and designate space exclusively for bicyclists, prevent speeding, reallocate roadway space, change land widths if needed
Aware/visible: make it easier for people driving to see people bicycling and vice versa – this is where geometry is key and pavement markings/signs can help
All ages and abilities: too stressful to take your child with you? Keep thinking about what would further reduce stress.

## Slide 10: Context Matters
PRINCIPLES
Motor Vehicle Speeds
Traffic Volume
Shared Spaces
Exclusive Lane Assignment
Physical Separation
Notes: The general breaking points or thresholds vary, but can look something like this:

## Slide 11: Management Strategies
Reconfigure Lanes
(Road Diet)
Remove On-Street Parking
Reduce Lane Width
Speed Hump, Table*
Mini Traffic Circle
Curb Extension
Median Island
PRINCIPLES
Signal Timing
Cul-de-sacs, Diverters
Non-motorized Cut-throughs
Speed
Volume
Speed & Volume
Notes: *Speed bumps, which more often resemble barrier curbs and parking stops, are not ideal for speeds above 5mph and are pretty much universally hated for transportation facilities.

## Slide 12: On Street, Midblock
Shared Lane / Yield Roadway
Advisory Shoulder / Advisory Bike Lane
Paved Shoulder
Pedestrian Lane
Bike Boulevard / Neighborhood Greenway
Bike Lane
Buffered Bike Lane
One-Way Separated Bike Lane
Left Side Bike Lane
Contra-flow Bike Lane
Two-Way Separated Bike Lane
Raised, Separated Bike Lane
ON STREET

## Slide 13: Shared Lane Marking
ON STREET
The “Sharrow”
Shows Intended Alignment of Bicyclist
Visual Reminder of Shared Space
Not intended for use on Bike Lanes or Paved Shoulders

## Slide 14: Shared Lane Marking
ON STREET
“For some streets, this may be the center of a shared travel lane.”
– AASHTO Bike Guide, Section 4.4.
Notes: Generally, these are placed 4’ on center from the face of curb with no parking, or 11’ on center from face of curb when adjacent to parking.
Section 4.4 “For some streets, this may be the center of a shared travel lane.”
High turnover
History of dooring crashes
Or in use on Bike Boulevards

## Slide 15: Paved Shoulder
2-4% Cross slope, typ.
  BDE/BLRS permits 4-6%, but impractical for bicycling
Helpful on rural/suburban roads
  Increases turn radius at intersections
  Roadway recovery, room to pull over
  Extends pavement life
  Snow storage, mail delivery
Key consideration
  Maintained by the agency of jurisdiction, unlike a sidewalk or shared use path
ON STREET
Image Source: Alta Planning + Design

## Slide 16: Paved Shoulder
IF you are adding paved shoulders and
IF your design guidance suggests rumble strips
THEN maintain a 4’ min. area between rumble strip and edge of pavement
THEN provide a 12’ gap every 40-60’ for evasive actions
ON STREET

## Slide 17: Advisory Bike Lane, Advisory Shoulder
ON STREET
Per AASHTO: 14’+ lane width
Popularized during vehicular cyclist movement
Almost always requires signage
  (W11-1 & W16-1 or R4-11)
Better solutions are available

## Slide 18: Advisory Bike Lane, Advisory Shoulder
ON STREET
Experimental Treatment
Two-Way Center Travel Lane
No center line
Suitable in Low speed, Low volume Environments
Yield to Bicyclists
Permissive broken lane line
Two-way Center Travel Lane
Optional Contrasting Paving Materials

## Slide 19
ON STREET
Bloomington, IN
Chicago, IL
Edina, MN
Notes: Applications can involve curb and gutter or open swale; with or without on-street parking.
FHWA Guidance: Use W6-3 sign to remind users of the two-way condition.
Do not mark a center line.
If you need to mark a center line around a curve, over a hill, or approaching an at-grade railroad crossing, widen the pavement to create paved shoulders and two travel lanes.
Refer to sight distance guidance based on speed from MUTCD.

## Slide 20: Pedestrian Lane
ON STREET
Experimental Treatment
Dedicated pedestrian space on roadway
Recommended as interim solution
Not shared with bicycles

## Slide 21: Pedestrian Lane
ON STREET
Must meet ADA for cross-slope, detectable warnings
Must meet PROWAG for running slope
W11-2 plus “ON ROADWAY” sign recommended
Flexible delineators suggested at cross streets to prevent encroachment by turning vehicles
Double Solid Line
Pedestrian
Lane Markings
High Visibility Crosswalk
Bicyclists Use Roadway
W11-1 Sign Assembly

## Slide 22: Bike Lane
ON STREET
Dedicated Space
Width
  4’ min. to edge of pavement
  5’ min. to face of curb
  NACTO recommends 6’ to face of curb (NACTO)
  Wider IF:
    Adjacent to parking without buffer
    On streets above 35mph

## Slide 23: Bike Lane
ON STREET
Ideal Placement
  25mph ≥ posted speed ≤ 35mph
  3k ≥ ADT ≤ 10k
Required:
  6” edge line adj. travel lane
  Bike lane symbol
Optional:
  4” edge line adj. gutter or edge of pavement
  Signs to supplement pavement markings

## Slide 24: Buffered Bike Lane
ON STREET
Buffer:
  1.5’ minimum, 2’ typical
  Hatch recommended if 3’ or wider
    30-45 degree angle
    10-40’ spacing (CDOT uses 20’)
    Posted speed is a good rule of thumb
Parking side vs. travel side
  Which hazard is more likely
  If you have room, add both

## Slide 25: Buffered Bike Lane
ON STREET
Organizes roadway space
  Bike lanes wider than 6’ begin to look like parking or travel lanes
Heavy vehicle-friendly
  The benefits of a 12’ lane without encouraging speeding
Crash mitigation
  Helps keep bicyclists out of dooring crash zone

## Slide 26: Buffered Bike Lane
ON STREET
12’ Travel
6’ Bike
6’ Walk
12’ Travel
5’ Bike
6’ Walk
2’
2.8’
4.3’
Notes: Note how the addition of a buffer helps improve channelization without doing anything else. This can be helpful when you are in a state or city with a 4’ minimum passing distance law on the books (like Illinois)

## Slide 27: Separated Bike Lane
ON STREET
Notes: AKA Cycle Tracks – explain the terminology (history of the use of “protected” versus separated)
Top Row: One-way, separated bike lanes, from left: Douglas Park, Chicago; Clybourn Avenue, Chicago; Clybourn Avenue, Chicago
Bottom Row: Two-way, separated, from left: Dearborn Street, Chicago; Clinton Street, Chicago; Chicago Avenue, Evanston.

## Slide 28: Separated Bike Lane
ON STREET
Vertical element separating bike lane from everything else
  Parking
  Barrier curb
  Mountable curb
  Median, planters
  Flexible delineators*
MUTCD Guidance?
  Not exactly
  Bicycle facility geometric guidance is based on preferential lane treatment (AASHTO), and thus not governed by MUTCD
Notes: *

## Slide 29: Separated Bike Lane One-Way
ON STREET
Best Resource? FHWA Separated Bike Lane Planning and Design Guide
Notes: *This shows a two-page spread of separation guidance, including spacing of curbs, delineators, or both.

## Slide 30: Separated Bike Lane One-Way
ON STREET
15’ min. clear visual sign triangle
20’ min. parking restriction
Green dash conflict marking: 2’ x 6’ bars (5.5’ green bar, 6” dotted white line, 2’ dash)
4’ C-C typ.
2’ spacing (4’ C-C)
vs.
6’ spacing (8’ C-C)
Curb vs. Pavement Marking
Notes: 2’ spacing, reminiscent of high-visibility pedestrian crosswalk markings, were typical at the time of creation of the FHWA guide. However, since that time, IA interpretation of green pavement markings for conflict zones has relaxed the spacing, resulting in 6’ spacing (and yielding material cost savings)

## Slide 31
Notes: Dodge Avenue, looking north approaching Kirk Street
Evanston, IL
Source: Google Street View

## Slide 32: Separated Bike Lane One-Way
ON STREET
Provides high quality, low-stress facility
Requires more space than conventional bike lanes
Creative interpretation of preferential lane design
Wait, why is the bike lane on the left side?
Notes: Good question: let’s get into this…

## Slide 33: Left Side Bike Lane
ON STREET
Required:
  5’ min. width, 6’ desired
  6” edge line, bike lane symbol
Optional:
  Left Lane Bike Lane Only
Recommended:
  Use two-stage turn boxes and/or signal separation for turns
  Variations on R10-15 sign
    “Left Turn Yield to Bikes” sign since this is a novel application
R10-15
R3
R1-5a variant*

## Slide 34: Contra-flow Bike Lane
ON STREET
Also helps accommodate wrong-way riding
Required:
  Double yellow
  One-way except bikes (R6-1)
  Bike lane word, symbol, or arrow (MUTCD 9-3 assembly)
  Signals
Optional:
  Two-way warning sign (W6-3)
R6-1 w/plaque
W6-3

## Slide 35
ON STREET
Notes: So let’s review the building blocks of a typical midblock section that includes a contraflow bike lane.
Essentially a two-way street
Contraflow bike lane is basically where an opposing lane of traffic would be on any typical two-way street.
  Left side placement mimics this, reducing potential conflicts to the same kind you would experience on any other two-way street (except that bicyclist speed, visibility, vulnerability are different)

## Slide 36
ON STREET

## Slide 37: Separated Bike Lane Two-Way
ON STREET
8-12’ bikeway, 3’ buffer (min.)
Separation (curb, cars, delineators)

## Slide 38
ON STREET
Dearborn Street, Chicago
Sheridan Road, Evanston

## Slide 39
ON STREET
Bike Lane = 7’
Buffer = 4’
Minimum Clear Width = 9.5’
Bike Lane = 7.5’
Minimum Clear Width = 7.5’

## Slide 40: On Street, Intersection (and Midblock)
Shared Right Turn and Bike Lane
Through Bike Lane
Bend In
Bend Out
Bike Box
Two-stage Turn Box
Protected Intersection
Intersection Crossing Markings*
Bike Signals
Mini Traffic Circle*
Roundabout
Median Refuge Island*
*Neighborhood Greenway
ON STREET

## Slide 41: Shared Right Turn Lane / Bike Lane
ON STREET
Places bike lane within alignment of a right-turn lane
Eliminates lateral shift for one user group (bicyclists)
Keeps bicyclist aligned left of where a right-turn conflict would arise

## Slide 42: Shared Right Turn Lane / Bike Lane
ON STREET
55th Street, Chicago, IL
Billings, MT
Notes: Design on the right also may be referred to as a mixing zone.

## Slide 43: Shared Right Turn Lane / Bike Lane
Required
  Bicycle symbol to clarify intended position
  9’ min. width, 13’ max.
    BDE/BLRS: Aux. lanes ≥ 10’
Optional
  Dashed line
  Shared lane
  Right turn only (R3-5r)
ON STREET

## Slide 44: Through Bike Lane
ON STREET
Lane continuity important
  Channelizes movements
  Eliminates right hook conflict
  Clarifies yielding responsibility
Required
  Edge line
  Bike lane symbol
Optional
  Skip dash (2’ dash, 6’ space)
  Signage R4-4, R3-7R
  Green Pavement

## Slide 45: Bend In
ON STREET
Bike lane bends in, toward travel lane.
Places users closer to each other before turn.
Note the lack of exclusive right turn lane.
Notes: Works well in lower speed (30 mph or slower) environments.
Signalized or unsignalized
Consider “Right turn yield to bikes” sign (modified R10-15)

## Slide 46: Bend Out
ON STREET
Bike lane bends out, away from travel lane.
Separates automobile turning movement from bike crossing movement.
Notes: Works well with higher speed environments (35mph)
Ideal bend out provides one car length of storage between travel lane and bike crossing.
Consider “Right turn yield to bikes” sign (modified R10-15)
Discuss whether you would want a bend out adjacent to a right-turn lane?

## Slide 47: Bend In vs. Bend Out
ON STREET
 | Pros | Cons
Bend In | Motorists more likely to see bicyclists in adjacent lane. Requires less space than a bend out. Can be done with or without curb work. | May require removal of one or two on-street parking spaces. Less robust separation can be stressful for some roadway users.
Bend Out | Allows turning motorist to get out of the travel lane before crossing the bike lane (reducing the occurrence of a rear end crash) Facilitates a two-stage left turn for bicyclists. If done with curb improvements, creates a pedestrian refuge, traffic calming effect. | Requires more space than a bend in (typically) Construction of curb work more costly, impact drainage, etc. Be careful to avoid cluttering the refuge, impacting sight lines.
Notes: Works well with higher speed environments (35mph)
Ideal bend out provides one car length of storage between travel lane and bike crossing.
Discuss whether you would want a bend out adjacent to a right-turn lane?

## Slide 48: Bike Box
ON STREET
Modified interpretation of a setback stop bar.
Provides room for groups of bicyclists to queuing at signalized intersections.
Doesn’t really facilitate left turns

## Slide 49: Two-stage Turn Box
ON STREET

## Slide 50: Bike Box
ON STREET
If you are trying to accommodate left turns, consider the bike box as a modification to the left turn lane.
Works well at signalized left turns or FYA conditions.
Less stressful than merging left to turn (re: AASHTO guidance).
Notes: Left turns in mixed traffic are stressful, even more so if there is no exclusive left turn lane.
Early uses of bike boxes involved uphill grades, signalized intersections, and predictable wait times.

## Slide 51: Two-stage Turn Box
Green pavement marking that shadows another lane group at a signalized intersection.
Splits a left turn into two movements.
Less stressful than moving left.
ON STREET

## Slide 52: Two-stage Turn Box
Can shadow a parking lane or travel lane on the cross street.
Requires no turn on red (R10-11) condition to mitigate turning conflicts
Currently an experimental treatment (MUTCD 1A.10)
ON STREET

## Slide 53: Two-stage Turn Box
Legitimizes a defensive bicyclist movement
ON STREET

## Slide 54
ON STREET

## Slide 55: Protected Intersection
ON STREET
Each user group’s path is channelized
Turning conflicts are mitigated through:
  Reduced turning radii
  Lower speeds
  Shorter crossing distances / exposure times

## Slide 56: Protected Intersection
ON STREET
Partial protection works, too.
  One or more legs of an intersection
  One or more movements through an intersection

## Slide 57: Intersection Crossing Markings
ON STREET
Clarify (and anchor) bicyclist and motorist paths through an intersection.
Especially helpful if there is a lateral shift or horizontal curve.
Green pavement recommended to highlight conflict / crossing / weaving segments

## Slide 58: Intersection Crossing Markings
ON STREET

## Slide 59: Bike Signals
ON STREET
Subject to Interim Approval (IA-16)
Provide exclusive phase for bicycle movement
Required on two-way, separated bike lanes or contraflow facilities

## Slide 60: Bike (or Traditional) Signals
ON STREET
If using pavement detection, consider pavement markings and loop detector design to accommodate bikes

## Slide 61: Beacons (and other Xing support)
ON STREET
IF you have a midblock crossing location and…IF you have determined the need for beacons*
Consider:
  RRFB
  HAWK
Pedestrian actuated
Complements other treatments

## Slide 62: Beacons (and other Xing support)
ON STREET
Crossing warning signage (W11 series)
  Assigns priority to path crossing users (warning signage)
  Education and periodic enforcement recommended
Stop or yield on path
  Smaller than roadway application
  MUTCD Section 2B, subject to engineering judgment

## Slide 63: Beacons (and other Xing support)
ON STREET
Crossing angle matters, too
Use curves to improve alignment and also slow approaching path users
Aim for right angles
Supplement with warning signs

## Slide 64: Mini Traffic Circle
ON STREET
Neighborhood-scale intersection element
  Min. 15’ curb-to-circle width
  Recommended in low-speed (25mph and below)
Can be enhanced with signage, pavement markings
  Branded as a bicycle boulevard or neighborhood greenway

## Slide 65: Roundabout
ON STREET
Two options, both involve termination of on-street bike lane:
  End bike lane, transition to shared lane, circulate single file with traffic
  Slip ramp onto sidewalk, widen sidewalk to shared use path (8-10’ typ.)
  Shared lane yield to bikes sign common

## Slide 66: Median Refuge Island
ON STREET
Barrier curb (or painted) median, provides room for crossing one lane or lane group at a time
IDOT draft application guidance based on speed, volume, and number of lanes
  Also informs when to supplement with signage, pavement markings, beacons
Notes: Note: The median refuge island has a crash modification factor (CMF) of 49%, relatively high. Sidewalks are 89%, among the highest CMF available.

## Slide 67: Neighborhood Greenway
Roadways that prioritize bicycle travel
  Uses traffic calming to keep motor vehicle speeds and volumes at a suitable level
    ≤ 3,000 ADT (≤ 1,500 preferred)
    ≤ 25 mph (≤ 20 mph preferred)
  Run parallel to a busy/stressful/direct route
  Maintains network connectivity
ON STREET

## Slide 68: Neighborhood Greenway
ON STREET
Notes: NACTO explains the reasoning behind the speed and volume thresholds, but FHWA, AASHTO, and ITE have been providing bike boulevard geometric, pavement marking, and signage guidance for a while.

## Slide 69: Neighborhood Greenway
Reorient Stop Signs
Speed Humps
Curb Extensions
Partial Closures
Median Diverters
Neighborhood Easements
ON STREET
Notes: In order:
Reorient stop signs (Portland, OR)
Speed humps (ASCE guidance)
Curb extension (Chicago, IL)
Partial closure (Portland, OR)
Median diverter (Portland, OR)
Neighborhood easement (Northbrook, IL)

## Slide 70: Neighborhood Greenway
ON STREET
Notes: In order:
Allen-Covenanter Greenway

## Slide 71: Off Street – Shared Use Path
10’ minimum, 12’ preferred
8’ acceptable for short distances
  A narrow segment is better than a gap
Stripe your shoulders and edge lines if you have high ADT or need to separate bicycle and pedestrian conflicts
  Otherwise, save a little $ on the project
OFF STREET

## Slide 72: Off Street – Shared Use Path
OFF STREET
Path: 10’
Shoulder: 2’
2ft. min
2ft. min

## Slide 73: Off Street – Sidepath
A sidepath is a shared use path that is within 5’ of a roadway, rail, or waterway edge.
AASHTO (and IDOT BDE) recommend 5’ minimum separation from traffic
  Wider separation may be needed adjacent to rail, steep grade changes,
OFF STREET
Notes: Image source: Lake County Division of Transportation / TrailLink.net
AASHTO is still the most comprehensive source for shared use path design, because not much has changed
- Where the biggest changes in guidance have occurred are at intersections. Refer to FHWA, NACTO, IDOT, and ITE for good guidance (specifically: bend in vs. bend out, crossing treatments, contextual guidance)

## Slide 74: Off Street –Transitions
OFF STREET
Notes: Note: this is mostly geometric improvements with some signs and pavement markings.
Image source (1): MassDOT Separated Bike Lane Planning & Design Guide
Image source (2): FHWA Small Town and Rural Multimodal Networks Guide

## Slide 75
Thank You
Questions + Discussion
Tim Gustafson, AICP | tgustafson@epsteinglobal.com | 312-429-8054