“ON CALL” MATERIAL TESTING SERVICES

PRELIMINARY SCOPE OF SERVICES

The consultant will provide laboratory and field material testing, and inspection assistance to Kane County Construction and Design staff with various items related to geotechnical soil and engineered material testing and applications.  The items listed here are to include but are not limited to:

Work to be conducted under an approved Work Order

- The Consultant will be required to perform standard ASTM field and laboratory tests at and or for various locations in Kane County via approved Work Orders as issued and approved by the Kane County Chief of Construction. The Work Order numbers will be the project section number or other ID tags as assigned by the County.  This project information will be included on all correspondences, reports and monthly invoices.

- Each Work Order proposal will include, at a minimum, a breakdown on all required staff, tests, frequencies, field, lab and report man hours and overall expected costs for each project.  The work order proposals will be reviewed and approved by Kane County’s Chief of Construction. Prior to any work by the consultant an initial coordination and parameter meeting with K.D.O.T. would be held either in person or via phone.

- The Consultant shall commence work immediately after Notice to Proceed is given either in writing or verbally with follow up documentation in writing.

Anticipated Services under this Contract

- Services will include but are not limited to: Plant and field sampling of concrete, Casting and testing cylinders or beams, Plant inspection, Sampling and analysis for HMA.  Nuclear density testing of HMA, Granular base and/or sub grade examination, testing and verification as directed, Unconfined compressive strengths of soils, exploratory soil boring, HMA and PCC pavement coring and testing and field monitoring of material placement and special projects as necessary and directed.

Staffing Concerns

- As much as possible, K.D.O.T. prefers to have the same staff member initially assigned to the Work Order, by the Material Consulting firm, conducting tests on the project to promote project continuity and uniformity. If this is not possible, the number of testing persons assigned to the project should be kept to a minimum.

- Any substitution or switching of staff shall be first approved by the Kane County Chief of Construction prior to implementation by the material consultant.

The K.D.O.T. reserves the right to request staffing changes for the interest of the project in the event of concerns regarding qualifications and/or testing procedures.

Monthly Reports Required

Work activity shall be summarized on either a daily or weekly basis, depending on project scope and activity. Each project report shall have, at a minimum, daily activity, test reports and site diagrams when necessary to adequately document testing activity. Further documentation such as Project reports and recommendations may be required as directed by KDOT.

Monthly billing of all Work Orders

  - Work performed under each approved Work Order will be billed on a monthly basis.

  - The consultant will provide monthly status summaries on all open Work Orders which will indicate:

    - The approved value of the Work Order.

    - Time and money spent within the billing month on a cumulative basis.

    - Estimated completion of the approved Work Order based on existing field conditions.

    - Remaining dollar balance on the approved Work Order.

    - An estimate of the Work Order status-i.e. adequate/inadequate funds to complete Work Order based on the initial agreed to amount.

The purpose of the above summary is to track and evaluate the dollars remaining on the annual testing contract.

Other Services may be requested

- The consultant may be asked to evaluate and recommend suitable engineering solutions to field issues as requested.

- Provide technical advice and information as requested.

- At the County’s request the consultant may be required to prepare project displays and reports for staff use or presentation purposes.

Records and Project Information

When available, Kane County may supply limited records to assist the consultant in the execution of work. This may include (when available):

- Design and/or Record drawings as available.

- Existing Highway right of way information

- Aerial Photography

.

A more detailed explanation of documentation and services may be found in the following County Scope of Engineering Services For Material Testing.

SCOPE OF ENGINEERING SERVICES FOR MATERIAL TESTING

THE MATERIAL TESTING CONSULTANT AGREES:

      - ( X )   Coordinate, furnish or cause to be furnished:

        - Proportioning and testing of concrete mixtures in accordance with the “Manual of Instructions for Concrete Proportioning and Testing” issued by the Bureau of Materials and Physical Research of the Illinois Department of Transportation and promptly submit reports on forms prepared by said Bureau.

        - Proportioning and testing of bituminous mixtures in accordance with the  “Manual of instructions for Bituminous Proportioning and Testing” issued by the Bureau of Materials and Physical Research of the Illinois Department of Transportation and promptly submit reports on forms prepared by said Bureau.

        - All compaction tests as required by the specifications or as directed by the DEPARTMENT and report promptly the same on forms prepared by the Bureau of Materials and Physical Research of the Illinois Department of Transportation.

        - Quality and sieve analysis on local aggregates that are not from approved producers (as listed by the Bureau of Materials and Physical Research of the Illinois Department of Transportation) to see that they comply with the specifications contained within the contract.

        - Inspect all materials when the Bureau of Materials and Physical Research of the Illinois Department of Transportation do not provide inspection at the source and submit inspection reports to the DEPARTMENT in accordance with the policies of the said DEPARTMENT.

The following Guidelines for Construction Procedures has been prepared to be used as a guide for prospective consultants during preparation of their Construction Supervision Contract Proposals. This outline will familiarize the consultant with Kane County Division of Transportation’s policies and procedures for construction supervision. This outline is a generalized list of policies and procedures mostly based on the Illinois Department of Transportation Division of Highways “CONSTRUCTION MANUAL” and also the specific requirements and needs of this agency.

    - DUTIES AND AUTHORITY OF THE  TESTING REPRESETATIVE

The Material Testing Engineer/Technician who from this point on shall be referred to, as the Testing Representative along with his/her staff is responsible for all required material/construction testing details on the project. The Materials Testing Representative shall be under the direct employment of Kane County. The Testing Representative  and Project Resident Engineer shall work together to coordinate, direct, and schedule all material inspection which will involve the type, frequency, and location as required by the I.D.O.T. Project Procedures Guide (Sampling Frequencies for Testing and Inspection) and/or the K.D.O.T.

The Testing Representative is expected to accept delegated responsibility and to make decisions within the authority delegated to him/her. A Testing Representative’s first duty is to enforce the contract and specification requirements. He/she shall perform all required field and material inspection and may need at times to maintain contact with the Contractor’s personnel to proficiently provide the engineering services necessary for the Contractor’s continued progress.

In addition the Testing Representative is expected to make the day-to-day recommendations to the extent that his/her experience and construction knowledge permit. However, the Testing Representative is not authorized nor should he/she attempt to revise, delete, or change the contract provisions. When contract, plan, or specification changes are anticipated the Testing Representative should contact the K.D.O.T. for guidance.

The Testing Representative Resident may be required to attend regular construction coordination meetings as determined by the RE or K.D.O.T.

The Testing Representative may at times be the K.D.O.T. public relations person when dealing with those whom the contract may involve and/or inconvenience and should act in a professional and courteous manner.

    - WORK ORDER INVOICES

All billings for material inspection services shall be submitted to both K.D.O.T and the project Ron a monthly basis. The project Resident Engineer shall check and verify correct dates, hours, and charges for service under the Work Order with the Project Diary. Any disparities shall be reported to K.D.O.T. as soon as possible. Copies of all material inspection billings shall be kept in the Resident’s file.

Materials inspection and documentation is the responsibility of the Materials Consultant.  However, the Resident Engineer and his/her staff shall verify that the quality, quantity, and frequency of all material inspection reports meet the requirements of I.D.O.T. (Bureau of Materials). Copies of completed material inspection reports shall be retained in the Resident’s file.

    - FINALING OUT OF PROJECTS

Once the Engineer’s Final Pay Estimate is submitted to I.D.O.T. for approval, the Bureau of Materials shall check all items for the required materials inspection and certification. The Resident Engineer shall receive a list of material deficiencies from the K.D.O.T.  The Resident Engineer then shall make a formal request to the Contractor and or the Materials Consultant for all needed material inspection and certification. Once the Resident receives all requested material inspection and certification, he/she shall submit it directly to I.D.O.T. (Bureau of Materials).